## Slide 1: Optomechanical sensing
Dr Christopher Baker
EQUS Autumn School, Noosa, May 9th 2024

## Slide 2: Basics of resonant sensing
Added mass
Added tension
Bare resonator

## Slide 3: Resonant sensing
The resonance frequency of the string is sensitive to changes in density and tension

## Slide 5
Sensitive to extremely minute changes in optical path length (separation between the mirrors)
Mechanical element can be functionalized to be made to interact with a wide range of stimuli
Notes: Use of precision interferometric readout provide greatly enhanced sensitivity
Mechanical elements can be functionalized to be made to interact with a whole host of stimuli

## Slide 6: Optical resonators come in various forms
Fabry-Perot cavities
Whispering gallery mode (WGM) resonators
Photonic crystal cavities

## Slide 7: Photonic crystal
mirror
mirror
cavity
Notes: 1D photonic crystal cavity

## Slide 8: 1D photonic crystal cavity
wavelength
reflection
mirror
mirror
cavity

## Slide 9: Whispering gallery mode resonators

## Slide 10: Whispering gallery mode resonators
Force
Acceleration
Magnetic fields
Electric fields
Temperature
Gases
Ultrasounds
Gravitational waves
Viscosity
Biological particles…
wavelength
transmission

## Slide 11: Optical quality factor
wavelength
transmission
→ Higher optical Q leads to improved sensitivity

## Slide 12: Optical quality factor
Material absorption Choose low loss material
Bending losses Use larger bend radius/ use higher refractive index material
Surface losses Control surface state (piranha, HF treatments, ALD…)
Sidewall roughness Multipass exposure, resist reflow…

## Slide 13: Material reflow
Silica microsphere
Silica microtoroid
GaAs microdisk
CaF2 resonator
Armani, D. K., Kippenberg, T. J., Spillane, S. M. & Vahala, K. J. Ultra-high- Q toroid microcavity on a chip. Nature 421, 925 (2003).

## Slide 14: Sensors
Magnetic fields
ultrasounds
Gravitational waves
acceleration
biosensors
Superfluid waves

## Slide 15
Signal
Change in optical path length
Readout

## Slide 16: Why use a resonator?
Notes: The resonator resonantly enhances the small phase shift occurring caused by the signal to be detected

## Slide 17: Gravitational waves
LIGO Scientific Collaboration and Virgo Collaboration et al., “Observation of Gravitational Waves from a Binary Black Hole Merger,” Phys. Rev. Lett., vol. 116, no. 6, p. 061102, Feb. 2016.
Notes: measure a change in distance 1,000 times smaller than the width of a proton

## Slide 18: magnetometry
B.-B. Li, J. Bílek, U. B. Hoff, L. S. Madsen, S. Forstner, V. Prakash, C. Schäfermeier, T. Gehring, W. P. Bowen, and U. L. Andersen, Quantum Enhanced Optomechanical Magnetometry, Optica, OPTICA 5, 850 (2018).
S. Forstner, S. Prams, J. Knittel, E. D. van Ooijen, J. D. Swaim, G. I. Harris, A. Szorkovszky, W. P. Bowen, and H. Rubinsztein-Dunlop, Cavity Optomechanical Magnetometer, Phys. Rev. Lett. 108, 120801 (2012).
S. Forstner, E. Sheridan, J. Knittel, C. L. Humphreys, G. A. Brawley, H. Rubinsztein-Dunlop, and W. P. Bowen, Ultrasensitive Optomechanical Magnetometry, Adv. Mater. 26, 6348 (2014).
→ With R=30um and Q=3x107
~0.01 Angstrom for linewidth shift

## Slide 19: accelerometry
A. G. Krause, M. Winger, T. D. Blasius, Q. Lin, and O. Painter, A High-Resolution Microchip Optomechanical Accelerometer, Nat Photon 6, 768 (2012).

## Slide 20
S. Basiri-Esfahani, A. Armin, S. Forstner, and W. P. Bowen, Precision Ultrasound Sensing on a Chip, Nature Communications 10, 132 (2019).
Ultrasound sensing

## Slide 21: Superfluid sensing
10 μm
New Journal of Physics, 18(12):123025, 2016

## Slide 22
Nature Physics 12, 788, 2016
Physical Review X, 6:021012, 2016
New J. Phys. 18, 123025, 2016.
New J. Phys. 21, 053029, 2019.
Science 366, 1480, 2019.
Nature Physics 16, 4 2020.
Optics Express, 28, 22450 2020. Npj Quantum Information 7, 1 2021.
Optics Express, 30, 30822 2022.
Science Advances 9 eade3591, 2023.

## Slide 23
W. W. Wasserman, R. A. Harrison, G. I. Harris, A. Sawadsky, Y. L. Sfendla, W. P. Bowen, and C. G. Baker, Cryogenic and Hermetically Sealed Packaging of Photonic Chips for Optomechanics, Optics Express, 30, 30822 Aug (2022).

## Slide 24: Superfluid wavetank

## Slide 27: Why use cleanroom nanofabrication?

## Slide 28: Why miniaturize?
Scalability / cost and power reduction & integration
Higher spatial resolution
Higher bandwidth
Higher sensitivity
Sansa, M. et al. Optomechanical mass spectrometry. Nature Communications 11, 3781 (2020).

## Slide 29: Biological/particle sensing using optical resonators
Frequency shift approach
Particle lands on resonator
→ Change in effective size
→ Dispersive shift
(fundamentally analogous to cavity optomechanics !)
particle
r

## Slide 30: Biological/particle sensing using WGM resonators
Frequency shift approach
Answer: 1- increase optical Q. 2- Decrease mode volume → High Q/V ratio
Example: use plasmonic resonance
E. Kim, M. D. Baaske, I. Schuldes, P. S. Wilsch, and F. Vollmer, “Label-free optical detection of single enzyme-reactant reactions and associated conformational changes,” Science Advances, vol. 3, no. 3, Mar. 2017.
Label-Free Detection of Single Protein Using a Nanoplasmonic-Photonic Hybrid Microcavity Venkata R. Dantham et al

## Slide 31: Small mode volume dielectric cavities
Hu, S. et al. Experimental realization of deep-subwavelength confinement in dielectric optical resonators. Science Advances 4, eaat2355 (2018).

## Slide 32: Choice of optical polarization
Choice of TE/TM modes
Baker, C. G. et al. New J. Phys. 18, 123025 (2016).

## Slide 33: Maximizing modal overlap
Almeida, V. R., Xu, Q., Barrios, C. A. & Lipson, M. Guiding and confining light in void nanostructure. Opt. Lett., OL 29, 1209–1211 (2004).
Harris, G. I. et al. Proposal for a quantum traveling Brillouin resonator. Opt. Express, OE 28, 22450–22461 (2020).

## Slide 34: Review articles
B.-B. Li, L. Ou, Y. Lei, and Y.-C. Liu, Cavity Optomechanical Sensing, Nanophotonics (2021).
Ward, J. & Benson, O. WGM microresonators: sensing, lasing and fundamental optics with microspheres. Laser & Photonics Reviews 5, 553–570 (2011).
Jiang, X., Qavi, A. J., Huang, S. H. & Yang, L. Whispering-Gallery Sensors. Matter 3, 371–392 (2020).

## Slide 35: Quantum limits to sensitivity
Standard quantum limit (SQL)

## Slide 36: Radiation pressure of light

## Slide 37: Radiation pressure
Kepler (1619)
Notes: Add mirror

## Slide 38: Radiation pressure
Kepler (1619)
Notes: Add mirror

## Slide 39: Radiation pressure
Photons carry momentum
Kepler (1619)
Notes: This mechanism arrises because, although they have no mass, photons carry momentum.

## Slide 40: Radiation pressure
Photons carry momentum
Kepler (1619)
Notes: This mechanism arrises because, although they have no mass, photons carry momentum.

## Slide 41: Radiation pressure
-Radiation pressure of sunlight (I=1 kW/m2) striking the earth at normal incidence,
Case 1: Absorbed
Case 2: Reflected
Pa
Pa
→~1010 times smaller than atmospheric pressure
Notes: Irradiance approx. 1 kW/m^2

## Slide 42: Experimental detection of radiation pressure
Crookes radiometer (1873)
Notes: The Crookes radiometer, also known as a light mill, consists of an airtight glass bulb, containing a partial vacuum. Inside are a set of vanes which are mounted on a spindle. The vanes rotate when exposed to light, with faster rotation for more intense light, providing a quantitative measurement of electromagnetic radiation intensity
Invented by a chemist, William Crookes in 1873

## Slide 43: Experimental detection of radiation pressure
Crookes radiometer (1873)
Which direction do the blades spin in ?
Notes: Not radiation pressure.
Wrong rotation direction
Works best around p=1Pa, Stops working in very high vacuum

## Slide 44: Experimental detection of radiation pressure
E. F. Nichols and G. F. Hull, ‘The pressure due to radiation," Proceedings of the American Academy of Arts and Sciences, vol. 38, no. 20, pp. 559-599, 1903.
Experimental detection
Nichols and Hull, 1901
Lebedew, P. (1901). "Untersuchungen über die Druckkräfte des Lichtes". Annalen der Physik. 311 (11): 433–458
Peter Lebedev
Notes: Torsional balance

## Slide 45: Standard quantum limit

## Slide 46: Standard quantum limit (SQL)
Measured photodetector intensity → resonator position
λL
Wavelength
Normalized transmission
T. J. Kippenberg and K. J. Vahala, Cavity Optomechanics: Back-Action at the Mesoscale, Science 321, 1172 (2008).

## Slide 47: Standard quantum limit (SQL)
Measured photodetector intensity → resonator position
λL
Wavelength
Normalized transmission
T. J. Kippenberg and K. J. Vahala, Cavity Optomechanics: Back-Action at the Mesoscale, Science 321, 1172 (2008).
λL
Wavelength
Normalized transmission
Influence of shot noise
!
Notes: Shot noise also occurs in photon counting in optical devices, where shot noise is associated with the particle natureof light.
n optics, shot noise describes the fluctuations of the number of photons detected (or simply counted in the abstract) because they occur independently of each other. This is therefore another consequence of discretization, in this case of the energy in the electromagnetic field in terms of photons.

## Slide 48
https://10m.aei.mpg.de/standard-quantum-limit-sql/
https://www.kth.se/social/files/5e8685f338d153ef15d4ee30/lecture-2-photon-statistics.pdf

## Slide 49: Standard quantum limit (SQL)
Time
Photodetector intensity
Shot noise
→ At the SQL, detector noise and quantum back-action noise contribute each a position uncertainty equal to half of the zero-point motion.
Photons imparts a random kicks, effect on momentum and position grow as = ‘backaction noise’
Notes: From AKM, Rev Mod Phys: The fluctuating radiation-pressure force (again, due to the photon
shot noise) imprints an unavoidable jitter on the mechanical
motion. Each of the photons imparts a random kick, and their
overall effect on the momentum and position will grow like
root N, as in a random walk. That effect is called backaction noise
and counteracts the increase of phase readout precision at large
N. Thus, there is an optimum at intermediate photon numbers,
where the sum of the two effects is minimal.
Standard quantum limit for continuous measurement
At the SQL,
detector noise and quantum back-action noise contribute
each a position uncertainty equal to half of
the zero-point motion of the mirror, where the latter
is given

## Slide 50: Observation of back-action noise
Purdy, T. P., R. W. Peterson, and C. A. Regal. “Observation of Radiation Pressure Shot Noise on a Macroscopic Object.” Science 339, no. 6121 (February 15, 2013)
Notes: Optical detection needs to be shot noise limited (technical noise, laser noise) this is ideal case but generally as power is increased unwanted effects, heating, etc cite Regal paper
However, for typical objects, the scale of quantum
back-action is small compared with thermal
motion or classical probing noise. In this Report,
we observe RPSN on a solid macroscopic (visible
to the naked eye) mechanical resonator by
using an optical interferometric measurement of
its vibrational motion.

## Slide 51: Photonic chip demo

## Slide 52
Gröblacher, S., Hill, J. T., Safavi-Naeini, A. H., Chan, J. & Painter, O. Highly efficient coupling from an optical fiber to a nanoscale silicon optomechanical cavity. Appl. Phys. Lett. 103, 181104 (2013).